PROBLEM
The problem is in the real time images, these star images are mostly corrupted by various noises (photon response uniform noise, photon shot noise, dark current noise, readout noise etc.) and also due to the relative motion between the star sensor and the stars.
Due to the large angular rate, the star point moves on the focal plane during the exposure time, which may lead to two changes for the star point:
1. The position shifting of the focal plane and
2. The limited starlight energy dispersing into more pixels.
There are two points to the motion blur problem:
1. If the angular rate is in the dynamic range of star sensor, simply denoising using some novel method can solve the problem
2. If the angular rate is larger than the dynamic range, we need to denoise and then proceed to restoration part.
SOLUTION
1. Denoising:
Let the corrupted image be g(x,y) and f(x,y) be the clear image of the same dimension (NxN), then
g(i,j) = f(i,j) + n(i,j)
where 0 ≤ i,j ≤ N-1 and n(i,j) is the additive random noise and independent of f(i,j) .
The goal is to remove n(i,j) and estimate f(i,j) which minimizes the Mean Squared Error.
Since f(i,j) is mostly distributed as a smooth signal at low frequency, while n(i,j) is distributed at high frequency, a two-dimensional discrete wavelet transform (DWT) can be implemented to transform g(i,j) into wavelet domain. The low frequency approximation subband will contain the low frequency portion of g(i,j) . Rest will be noise.
I am currently learning about discrete wavelet transforms.
2. Restoration
Model the corrupted image g(x,y) as mathematical model and also, find a model for the Point Spread function (PSF) of the image and call it h(x,y) .
The relation between the corrupt image, the clear image and the PSF model in frequency domain is given by:
G(u,v) = F(u,v) H(u,v)
Where, G(u,v) , F(u,v) and H(u,v) are Fourier transforms of g(x,y), f(x,y) and h(x,y) respectively.

However, the noise n(x,y) is typically unknown in practice and the classical wiener filter is problematic, we use the modified Wiener filter which is given by:
F^(u,v)= {{H} ^ {'} left (u,v right )} over {H left (u,v right ) {H} ^ {'} left (u,v right )} G(u,v)
Here, H'(u,v) denotes the complex conjugate of H(u,v) and F^(u,v) is the estimate of F(u,v) .
Finally, from F^(u,v) , we can calculate f^(x,y) , an estimate of f(x,y) by taking Inverse Fourier transform.
KSB method
https://books.google.co.in/books?id=w-5EnuOC3C0C&pg=PA296&lpg=PA296&dq=KSB+method+implementation&source=bl&ots=PJ9o434n2G&sig=s_VJvU2IhAUsC4466fiF1o_-Drc&hl=en&sa=X&ved=0CEgQ6AEwB2oVChMImJbv18TRyAIVRAiOCh0m-A-d#v=onepage&q=KSB%20method%20implementation&f=false

# Advances in Machine Learning and Data Mining for Astronomy
 edited by Michael J. Way, Jeffrey D. Scargle, Kamal M. Ali, Ashok N. Srivastava

The seeing ranged from 1”.2 to more than 3”. We discarded images with poor signal-to-noise ratio (S/N;
mostly due to thin clouds) and images with tracking problems (where the stars are non-spherical and stretch more than a few pixels during the exposure), an excess of hot pixels, or a background gradient across the image. Finally, 78 U-band images were kept.

Abstract to ASI:
Image improvement and restoration in optical time series

Successful differential photometry of crowded fields requires images to be of a relatively uniform quality. Modern DIA (Differential Imaging Analysis) techniques usually take care of effects of variable atmospheric extinction and exposure times, and the methods even work better as the crowding increases, because in denser fields more pixels contain information about the PSF difference. However, if a time series is taken over long baselines, other sources of noise can creep in and worsen the images, such as e.g. PSF anisotropy, or smearing, which DIA usually cannot handle even for moderately elongated PSFs. This mostly happens due to either strong winds during the exposure or due to incorrect orientation of lenses in the image sensor device. This causes stars to be out-of-shape and out-of-focus, thereby making it improper to use in the subtraction process of DIA because these “corrupt” images lead to false positive results of variability/transients. In most of the studies that use DIA, these images are removed from the data set. However, when the observing program is over a long baseline and the exposures are taken at a low cadence, each image becomes very important as it is not possible to repeat them. Here we investigate several algorithms such as e.g. Richardson-Lucy Algorithm, Maximum Entropy Method and KSB method to correct such images to restore the circular shapes of stars as a first step, in order to minimize data loss in the currently run programs based on optical time series.

http://stsdas.stsci.edu/documents/SUG/UG_29.html#HEADING102
## Overview of Image Restoration
and they do use the Wiener filter also:
## Algorithms and Methods in STSDAS
Several restoration algorithms are provided in the STSDAS restore package. These algorithms, as implemented in STSDAS, are described in some detail in Chapter 12 of the HST Data Handbook. Summary descriptions of the following algorithms are provided in the next subsections:
- Richardson-Lucy algorithm: the lucy task
- Maximum Entropy Method: the mem task
- s-CLEAN algorithm: the sclean task
- Wiener filter and Fourier inverse filter: the wiener task
- Adaptive filters: the hfilter and adaptive task
All of these tasks are described in detail in the on-line help for each task.

Richardson-lucy didn’t help much